Roll No:

MODEL EXAM

Third Semester

Mechanical Engineering

ME3391 Engineering Thermodynamics

Date: 23.12.2023                       	             			                        Session    : FN

Time: 3Hrs                                                                                                                 Maximum:  100 marks

Answer ALL Questions

PART - A (10 X 2 = 20 marks)

| Q.NO | Questions | Marks | CO | BL | PO |
| --- | --- | --- | --- | --- | --- |
| 1 | Distinguish between Open and Closed systems. | 2 | CO1 | L4 | 1 |
| 2 | State Zeroth law and First law of thermodynamics. | 2 | CO1 | L1 | 1 |
| 3 | State the Kelvin–Planck statement of second law of thermodynamics. | 2 | CO2 | L1 | 1 |
| 4 | State Clausius statement of Second law of Thermodynamics. | 2 | CO2 | L1 | 1 |
| 5 | What is the principle of increase in entropy? | 2 | CO3 | L1 | 1 |
| 6 | What is Helmholtz free energy function? | 2 | CO3 | L1 | 1 |
| 7 | Draw a P-T (pressure-temperature) diagram for a pure substance. | 2 | CO4 | L2 | 1 |
| 8 | Difference between ‘flow process’ and ‘non-flow process’. | 2 | CO4 | L4 | 1 |
| 9 | What is Maxwell equation? | 2 | CO5 | L1 | 1 |
| 10 | Write down two Tds relations. | 2 | CO5 | L2 | 1 |

PART- B (5 X 13 = 65 marks)

| Q.NO | Questions | Marks | CO | BL | PO |
| --- | --- | --- | --- | --- | --- |
| 11. | (a). In a Carnot heat engine 50g of air acts as the working substance. The peak cycle temperature is 930 K and the maximum pressure is 8.4x 103 kPa. The heat addition per cycle is 4.2 kJ. Determine the maximum cylinder volume if the minimum temperature during the cycle is 315 K. | 13 | CO1 | L5 | 1 |
|  | Or |  |  |  |  |
|  | (b). A reciprocating air compressor takes in 2 m3 /min air at 0.11 MPa, 293 K which it delivers at 1.5 MPa, 384 K to an after cooler where the air is cooled at constant pressure to 298 K. The power absorbed by the compressor is 4.15 kW. Determine the heat transfer in (i) the compressor (ii) the cooler. State your assumptions. | 13 | CO1 | L5 | 1 |
| 12. | (a). A reversible engine operates between a source at 972ºC and two sinks, one at 127ºC and another at 27ºC. The energy rejected is same at both the sinks. What is the ratio of heat supplied to the heat rejected? Also calculate the efficiency. | 13 | CO2 | L5 | 1 |
|  | Or |  |  |  |  |
|  | (b). An engine is supplied with 1120 kJ/s of heat. The source and sink temperature are maintained at 560 K and 280 K. Determine whether the following cases represent the reversible, irreversible or impossible heat engines. (1) 900 kW of heat rejected (2) 560 kW of heat rejected (3) 108 kW of heat rejected | 13 | CO2 | L5 | 1 |
| 13. | (a). In a closed system air is at a pressure of 1 bar, temperature of 300 K and volume of 0.025 m3 . The system executes the following processes during the completion of thermodynamic cycle: 1-2; constant volume heat addition till pressure reaches 3.8 bar, 2- 3; constant pressure cooling of air, 3-1; isothermal heating to initial state. Determine the change in entropy in each process. Take Cv = 0.718 kJ / kg K, R=287 J/kgK. | 13 | CO3 | L5 | 1 |
|  | Or |  |  |  |  |
|  | (b). A reversible heat pump is used to maintain a temperature of 0o C in a refrigerator when it rejects the heat to the surroundings at 25o C. If the heat removal rate from the refrigerator is 1440 kJ / min, determine the C.O.P. of the machine and work input required. | 13 | CO3 | L5 | 1 |
| 14 | (a). Two streams of steam, one at 2 MPa, 3000 C and the other at 2 MPa, 4000 C, mix in a steady flow adiabatic process. The rates of flow of the two streams are 3 kg/min and 2 kg/min respectively. Evaluate the final temperature of the emerging steam, if there is no pressure drop due to the mixing process. What would be the rate of increase in the entropy of the universe? This steam with negligible velocity now expands adiabatically in a nozzle to a pressure of 1 kPa. Determine the exit velocity of the stream and exit area of the nozzle. | 13 | CO4 | L5 | 1 |
|  | Or |  |  |  |  |
|  | (b).A rigid tank of 0.03m3 capacity contains wet vapour at 80 KPa. If the wet vapour mass is 12kg, calculate the heat added and the quality of the mixture when the pressure inside the tank reaches 7 Mpa. | 13 | CO4 | L5 | 1 |
| 15 | (a). Derive Tds equation when T and V independent ii) T and P independent iii) P and V independent | 13 | CO5 | L2 | 1 |
|  | Or |  |  |  |  |
|  | (b). Derive Maxwell relations and explain their importance in thermodynamics. | 13 | CO5 | L2 | 1 |

PART- C (1 X 15 = 15 marks)

| Q.NO | Questions | Marks | CO | BL | PO |
| --- | --- | --- | --- | --- | --- |
| 16. | (a). Derive the Vander waal’s equation. | 15 | CO5 | L2 | 1 |
|  | Or |  |  |  |  |
|  | (b). In steam generator compressed water at 10 MPa, 300 C enters a 30 mm diameter tube at the rate of 3 litres /sec. Steam at 9 MPa and 4000C exit the tube. Find the rate of heat transfer. | 15 | CO4 | L5 | 1 |

| BT LEVEL | CO1 | CO2 | CO3 | CO4 | CO5 | % |
| --- | --- | --- | --- | --- | --- | --- |
| Remember | Q. Nos | 2 | 3,4 | 5,6 |  | 9 | 6.66 |
|  | Marks | 02 | 04 | 04 |  | 02 |  |
| Understand | Q. Nos |  |  |  | 7 | 10, 15 (a), 15 (b),16 (a) | 25 |
|  | Marks |  |  |  | 02 | 43 |  |
| Apply | Q. Nos |  |  |  |  |  |  |
|  | Marks |  |  |  |  |  |  |
| Analyze | Q. Nos | 1 |  |  | 8 |  | 2.23 |
|  | Marks | 02 |  |  | 02 |  |  |
| Evaluate | Q. Nos | 11 (a), 11 (b) | 12 (a), 12 (b) | 13 (a), 13 (b) | 14 (a), 14 (b), 16 (b) |  | 66.11 |
|  | Marks | 26 | 26 | 26 | 41 |  |  |
| Total | 30 | 30 | 30 | 45 | 45 | 100 |

| IQAC Member | HOD / Mech |
| --- | --- |