Roll No:

MODEL EXAM

Third Semester

Mechanical Engineering

ME3391 Engineering Thermodynamics

Date: 23.12.2023                       	             			                       Session    : FN

Time: 3Hrs                                                                                                                 Maximum:  100 marks

Answer ALL Questions

PART - A (10 X 2 = 20 marks)

| Q.NO | Questions | Marks | CO | BL | PO |
| --- | --- | --- | --- | --- | --- |
| 1 | Define Path function. | 2 | CO1 | L1 | 1 |
| 2 | Explain homogeneous and heterogeneous system. | 2 | CO1 | L2 | 1 |
| 3 | Define Heat pump. | 2 | CO2 | L1 | 1 |
| 4 | Define Heat engine. | 2 | CO2 | L1 | 1 |
| 5 | Define irreversibility. | 2 | CO3 | L1 | 1 |
| 6 | List the causes on entropy increase. | 2 | CO3 | L1 | 1 |
| 7 | Difference between saturated fluid and compressed fluid. | 2 | CO4 | L4 | 1 |
| 8 | Explain the change of phase of water in T-v diagram. | 2 | CO4 | L2 | 1 |
| 9 | Define sensible heat of water. | 2 | CO5 | L1 | 1 |
| 10 | Define the term “super heat enthalpy’’. | 2 | CO5 | L1 | 1 |

PART- B (5 X 13 = 65 marks)

| Q.NO | Questions | Marks | CO | BL | PO |
| --- | --- | --- | --- | --- | --- |
| 11. | (a). A centrifugal pump delivers 2750 kg of water per minute from initial pressure of 0.8 bar absolute to a final pressure of 2.8 bar absolute. The suction is 2 m below and the delivery is 5 m above the centre of pump. If the suction and delivery pipes are of 15 cm and 1.0 cm diameter respectively, make calculation for power required to run the pump. | 13 | CO1 | L5 | 1 |
|  | Or |  |  |  |  |
|  | (b). Derive the equation for the work done, change in internal energy, and heat transferred for the following process (i) Isobaric, (ii) Isochoric, (iii) Isothermal (iv) Isentropic and (v) Polytropic. | 13 | CO1 | L2 | 1 |
| 12. | (a). A heat pump working on the Carnot cycle takes in heat from a reservoir at 323 K and delivers heat to a reservoir at . A heat engine is driven by a source at 1173 K and rejects heat to a reservoir at 333 K. The reversible heat engine, in addition to driving the heat pump, also drives a machine that absorbs 30 kW. If the heat pump extracts 17 kJ/s from the 323 K reservoir, determine (1) the rate of heat supply from the 1173 K source, and (2) the rate of heat rejection to the 333 K sink. | 13 | CO2 | L5 | 1 |
|  | Or |  |  |  |  |
|  | (b). A heat engine operating between two reservoirs at 100 K and 300 K is used to drive heat pump which extracts heat from the reservoir at 300 K at a rate twice that at which engine rejects heat to it. If the efficiency of the engine is 40% of the maximum possible and the co-efficient of performance of the heat pump is 50% of the maximum possible, make calculations for the temperature of the reservoir to which the heat pump rejects heat. Also work out the rate of heat rejection from the heat pump if the rate of supply of heat to the engine is 50 kW. | 13 | CO2 | L5 | 1 |
| 13. | (a). 5 m3 of air at 2 bar, 27o C is compressed up to 6 bar pressure following pv1.3 = constant. It is subsequently expanded adiabatically to 2 bar. Considering the two processes to be reversible, determine the network, net heat transfer, and change in entropy. Also plot the processes on T-S and P-V diagrams. | 13 | CO3 | L5 | 1 |
|  | Or |  |  |  |  |
|  | (b). In a Carnot heat engine 50g of air acts as the working substance. The peak cycle temperature is 930 K and the maximum pressure is 8.4x 103 kPa. The heat addition per cycle is 4.2 kJ. Determine the maximum cylinder volume if the minimum temperature during the cycle is 315 K. | 13 | CO3 | L5 | 1 |
| 14 | (a). A vessel of volume 0.04m3 contains a mixture of saturated water and steam at a temperature of 2500 C. The mass of the liquid present is 9 kg. Find the pressure, mass, specific volume, enthalpy, entropy and internal energy. | 13 | CO4 | L5 | 1 |
|  | Or |  |  |  |  |
|  | (b). Steam at a pressure of 15bar and 2500 C expands according to the law pV1.25=C to a pressure of 1.5 bar. Evaluate the final conditions, work done, heat transfer and change in entropy. The mass of the system is 0.8kg. | 13 | CO4 | L2 | 1 |
| 15 | (a). Explain joule –Kelvin effect. What is inversion temperature? | 13 | CO5 | L2 | 1 |
|  | Or |  |  |  |  |
|  | (b). Derive Maxwell’s equations and write down the first and second law Tds equations | 13 | CO5 | L2 | 1 |

PART- C (1 X 15 = 15 marks)

| Q.NO | Questions | Marks | CO | BL | PO |
| --- | --- | --- | --- | --- | --- |
| 16. | (a). Derive the clausis-clapey Equation. | 15 | CO5 | L2 | 1 |
|  | Or |  |  |  |  |
|  | (b). Explain the work done and heat transfer in Non-flow process with neat sketch. | 15 | CO4 | L2 | 1 |

| BT LEVEL | CO1 | CO2 | CO3 | CO4 | CO5 | % |
| --- | --- | --- | --- | --- | --- | --- |
| Remember | Q. Nos | 1 | 3,4 | 5,6 |  | 9,10 | 7.8 |
|  | Marks | 02 | 04 | 04 |  | 04 |  |
| Understand | Q. Nos | 2,11 (b) |  |  | 8,14 (b), 16 (b) | 15 (a), 15 (b),16 (a) | 47.76 |
|  | Marks | 15 |  |  | 30 | 41 |  |
| Apply | Q. Nos |  |  |  |  |  |  |
|  | Marks |  |  |  |  |  |  |
| Analyze | Q. Nos |  |  |  | 7 |  |  |
|  | Marks |  |  |  | 02 |  | 1.11 |
| Evaluate | Q. Nos | 11 (a) | 12 (a), 12 (b) | 13 (a),13 (b) | 14 (a) |  |  |
|  | Marks | 13 | 26 | 26 | 13 |  | 43.33 |
| Total | 30 | 30 | 30 | 45 | 45 | 100 |

| IQAC Member | HOD / Mech |
| --- | --- |